## Slide 1: Digital Integrated Circuits
Georgiana SIMION
2021/2022

## Slide 2: TTL – Usage Rules
Can be applied to other families (carefully)
It is forbidden to connect two or more outputs together
It is forbidden to connect the outputs to GND or VCC
Way to connect two TTL outputs

## Slide 3: Usage Rules
No input can be let floating
No input can be let unconnected
  Pull-up resistor
Rp

## Slide 4: Usage Rules
  pull-down resistor

## Slide 5: Usage Rules
  Interconnect several inputs (from the same gate):
    Advantage: simplicity,
    Disadvantage: low performance (Why?)
  For example,
      IiL_OR_A = IiL_NOR_A = 3 IiL,
      IiH_OR_A = IiH_NOR_A = 3 IiH,
      IiL_NAND_A = IiL_AND_A = IiL ,
      IiH_NAND_A = IiH_AND_A = 3 IiH
Notes:   Conectarea intrărilor nefolosite la intrări folosite: avantajul acestei metode este simplitatea, nemaifiind necesară rezistenţa RP. Dezavantajele metodei sunt legate de multiplicarea capacităţii de intrare Ci şi a curenţilor de la intrare în starea SUS, iar suplimentar pentru porţile SAU şi SAU-NU şi multiplicare curenţilor de intrare în starea JOS.

## Slide 6: Usage Rules
Unused gates – inputs must be connected also
Handling - ESD
Decoupling is mandatory.

## Slide 7: Usage Rules
High switching supply current
Decoupling
Solving for C yields:
But
So:

## Slide 8: Decoupling
ICC >= 15 ICC_NAND
C = 50 ... 100 nF
C near each IC

## Slide 9: Applications – driving loads with totem-pole outputs

## Slide 10: Driving a LED
Widely used
5 mm LED - Ud= 1.7 ... 2 V @ 10 mA
SMD LEDs-3-5 mA
I0L =16 mA >> I0H =0,8 mA

## Slide 11: HOMEWORK
Schematic design

## Slide 12: Driving higher currents
u0 = U0L (Tr OFF); u0 = U0H (Tr ON - sat)
ForT1: (Ic results 80 ... 300 mA)

## Slide 13: Driving higher currents
For T2 (Ic >= 1A):
Usually R2 = 1 k (why?); verify I0HMax

## Slide 14: Driving higher currents
Using a n MOS transistor (may be SMD)
Low rds
Heatsink (?)
R3 (?)

## Slide 15: Homework
Automotive bulb, 12 V/5A
  Select the Darlington / MOS transistor
  Compute PD
  Choose a heatsink

## Slide 16: TTL Three State Circuits

## Slide 17: 3 state gates
Homework: Datasheets for all 3 state gates; study 74xx244

## Slide 18: Schematic
Have also an Enable (EN or nEN) input
If EN = 0, y = HiZ

## Slide 19: Three State Gates
If nEN = 0, y = /A
If nEN = 1, y = A
I0ZM =  40A

## Slide 20: Three state circuits
1 bit wide bus
N bits wide bus:
    Data Bus
    Address bus
    Control Bus
    Combinations of above busses

## Slide 21: 1 bit wide bus

## Slide 22: Three state circuits
We can interconnect inputs (receivers) and only 3-state outputs (transmitters)
Rules
    Only one transmitter active: , ie.
    Only one transmitter active even when switching, so: tpNZ < tpZN
    Current balance (inputs and outputs)

## Slide 23: Evaluating tpNZ and tpZN

## Slide 24: Bidirectional transmission line
If DIR = 0, A -> B,
If DIR = 1, B -> A

## Slide 25: TRIGGER SCHMITT circuits

## Slide 26: TRIGGER SCHMITT circuits
Purpose:
  allowingtf > 100 ns
  Higher noise margin (compared to Uz =  0,4V)
Architecture: include a Schmitt circuit in an inverter

## Slide 27: TRIGGER SCHMITT circuits
The circuit triggers when each trigger level (Low and High) is met in the right direction: (Up ↑and Low ↓)
Former implementations: tranzistors, OpAmps, TTL, CMOS, etc

## Slide 28: TTL TRIGGER SCHMITT circuit
Positive feedback speeds the switching process
The transfer characteristic (transistor circuit):
The hysteresis is: Uhist = UTH - UTL

## Slide 29: Trigger Schmitt schematic (74132)

## Slide 30: Transfer Characteristic
  Why?

## Slide 31: TTL Trigger Schmitt examples

## Slide 32: Parameters
Threshold Voltages (7414, 7413, 74132): UPJos = 1,1 V şi UPSus = 1,9 V
Noise margin:
  UZH = UPJos - U0Hmin = 1,1 - 2,4 = - 1,3V
  UZL = UPSus - U0LMax = 1,9 - 0,4 = 1,5V
Better results

## Slide 33: Trigger Schmitt - Applications
Input interface for noisy environments

## Slide 34: LF Signal Interface
Input interface for low frequency signals

## Slide 35: Delay Circuit
Simple delay circuits
  Gen1 acts like a gate (V0L = 200 mV, V0H = 3,6 V)

## Slide 36: Delay circuit - timing

## Slide 37: Delay Circuit
You know already:
For charging C:
;
so:
ie:

## Slide 38: Delay Circuit
For discharging C,
;
so:
ie
Homework: Compare the simulation and analytical results

## Slide 39: Trigger Schmitt - Applications
Edge detection
Signal generation
Homework: Find schematics for these applications

## Slide 40: Other series

## Slide 41: Schottky (S)
74Sxxx
Uses Schottky transistors
The Schottky diode
  Ud = 0,3  0,4V.
  Fast switching time: tc = 1 ns.

## Slide 42: The Schottky Transistor
Cannot be saturated

## Slide 43: TTL Schottky (S)
Good performance: tp= 3 ns, PD = 20mW
Higher U0L: U0LMax = 0,5V

## Slide 44: Schematic – 74S00

## Slide 45: Simulation – 74S04

## Slide 46: The Simulated Transfer Characteristic

## Slide 47: Low Power Schottky (LS)
74LSxxx
Widely used
Low tp, low Pd
Schottky diodes on the input

## Slide 48: Schematic – 74LS00

## Slide 49: Schematic – role of elements
R2E – nonlinear
T4 + T5 = Darlington, (faster L-> H transition)
(Why)

## Slide 50: h21E- ic Plot

## Slide 51: Non-linear resistorR2E
Figura 3.48
Homework: simulate the above characteristicR2E – U3BE

## Slide 52: The transfer characteristic

## Slide 53: Schematic- CircuitMaker

## Slide 54: The simulated transfer characteristic

## Slide 55: 74ASxxx;74ALSxxx Series
Better technology, same schematic
Smaller components – faster chips
AS
  tp = 1,7; PD = 8 mW, ceea ce
  IiLMax = 2mA şi IiHMax = 0,2mA
  U0LMax = 0,5 V; U0Hmin = 2,7 V
ALS
  tp = 4 ns, PD = 1,2 mW,

## Slide 56: Input and Output Currents
Family | Output |  | Input | 
 | I0HMax | I0LMAx | IiHMax | IiLMax
74 | - 0,8 mA | 16 mA | 40 A | - 1,6 mA
74S | - 1 mA | 20 mA | 50 A | - 2 mA
74AS | -2 mA | 20 mA | 20 A | - 0,5 mA
74LS | - 0,4 mA | 8 mA | 20 A | - 0,4 mA
74ALS | - 0,4 mA | 8 mA | 20 A | - 0,1 mA
74F | - 1 mA | 20 mA | 20 A | - 0,6 mA

## Slide 57: Main parameters of the TTL family
Parameter Family | 74 | 74S | 74AS | 74LS | 74ALS | 74F
Dynamic parameter |  |  |  |  |  | 
Propagation delay[ns] | 9 | 3 | 1,7 | 9,5 | 4 | 3
Dissipated power [mW] | 10 | 20 | 8 | 2 | 1,2 | 6
…[pJ] | 90 | 60 | 13,6 | 19 | 4,8 | 18
Maximum frequency [MHz] | 35 | 125 | 200 | 45 | 70 | 100
Fan-Out (în cadrul aceleiaşi serii) | 10 | 20 | 40 | 20 | 20 | 33
Voltage levels |  |  |  |  |  | 
V0Hmin | 2,4 | 2,7 | 2,5 | 2,7 | 2,5 | 2,5
V0LMax | 0,4 | 0,5 | 0,5 | 0,5 | 0,5 | 0,5
ViHmin | 2,0 | 2,0 | 2,0 | 2,0 | 2,0 | 2,0
ViLMax | 0,8 | 0,8 | 0,8 | 0,8 | 0,8 | 0,8

## Slide 58
9) Ten TTL loads per TTL driver is known as:
a) noise immunity b) fan-out c) power dissipation d) propagation delay
10) What is the standard TTL noise margin?
a) 5.0 V b) 0.0 V c) 0.8 V d) 0.4 V
11) The time needed for an output to change from the result of an input change is known as:
a) noise immunity b) fan-out c) propagation delay d) rise time
12) Totem-pole outputs _____ be connected _____ because _____.
a) can, in parallel, sometimes higher current is required
b) cannot, together, if the outputs are in opposite states excessively high currents can damage one or both devices
c) should, in series, certain applications may require higher output voltage
d) can, together, together they can handle larger load currents and higher output voltages
13) What should be done to unused inputs on TTL gates?
a) They should be left disconnected so as not to produce a load on any of the other circuits and to minimize power loading on the voltage source.
b) All unused gates should be connected together and tied to V through a 1 komega.gif resistor.
c) All unused inputs should be connected to an unused output; this will ensure compatible loading on both the unused inputs and unused outputs.
d) Unused AND and NAND inputs should be tied to VCC through a 1 komega.gif resistor; unused OR and NOR inputs should be grounded.